## Slide 1: EG431D Data Acquisition
Introduction to MCU and Arduino Development Platform

## Slide 2: Objectives
Describe the embedded system development process with MCUs.
Explain Arduino’s significance in IoT and prototyping.
Understand Arduino IDE’s cross-compatibility and application scalability.
Learn to install libraries for Arduino projects.
Compile, upload, and execute a sketch on an Arduino Board.

## Slide 3: What is an MCU?
Compact data processing system with CPU, memory, and I/O peripherals.
Handles real-time data processing.
Key roles in sensor-based applications, motor controls, and signal analysis.
Supports communication protocols like UART, SPI, and I2C.

## Slide 4: Introduction to Arduino IDE
Open-source, user-friendly platform.
Simplifies MCU programming with C.
Key components: text editor, compiler, serial terminal, and application loader.
Facilitates rapid prototyping.

## Slide 5: Setting Up Your Workspace
Create a folder named “EG431D” on your desktop.
Inside, create a sub-folder named “libraries” for custom libraries.
Backup your directory at the end of each session.

## Slide 6: Exploring the Arduino IDE
Open the Arduino IDE from the desktop icon.
Set preferences to link to your EG431D folder.
Key tools: text editor, compiler, serial terminal.

## Slide 7: Installing Board Support
Open Board Manager (Tools > Board > Board Manager).
Search for “Arduino SAMD Boards” and install.
Connect Arduino MKR WiFi 1010 via USB.

## Slide 8: Creating and Saving a Sketch
A sketch is an Arduino program.
Create a new sketch (File > New).
Save the sketch in your EG431D directory.

## Slide 9: Installing Libraries
Open Library Manager (Sketch > Include Library > Manage Libraries).
Search for “blink” to find a StatusLED library.
Install the library and verify installation.

## Slide 10: Compiling and Uploading a Sketch
Open an example sketch (File > Examples > Blink).
Save, compile, and upload to the Arduino board.
Verify functionality by observing the blinking LED.

## Slide 11: Review Questions
What is the time for one complete LED blink?
How is the blink time set in the code?
How would you modify the code for a 1-second blink cycle?