## Slide 1: EG431D Data Acquisition
Frequency Domain Analysis

## Slide 2: Objectives
Learning Objectives:
  Describe the process of analyzing stationary and non-stationary signals in the frequency domain.
  Explain the fundamental principles of Fourier Transform, FFT, and STFT.
  Demonstrate practical applications of frequency domain analysis in real-world scenarios.
Key Applications:
  Audio processing
  Biomedical signal analysis
  Machine vibration analysis

## Slide 3: Introduction to Frequency Domain Analysis
What is Frequency Domain Analysis?
  Focuses on understanding the frequency components of a signal.
  Decomposes signals into sinusoidal components (frequencies, amplitudes, phases).
Comparison with Time-Domain:
  Time-domain: Amplitude vs. Time.
  Frequency-domain: Amplitude vs. Frequency.
Core Mathematical Tool: Fourier Transform.

## Slide 4: Fourier Transform and FFT
Fourier Transform (FT):
  Converts time-domain signal x(t) to frequency-domain X(f).
  Represents signals as a sum of sinusoids.
Discrete Fourier Transform (DFT):
  Sampled version of FT for discrete signals.
Fast Fourier Transform (FFT):
  Efficient algorithm for computing DFT.
  Reduces complexity from O(N2) to O(NlogN).
Applications:
  Spectral analysis, filtering, and system characterization.

## Slide 5: FFT Algorithm
Radix-2 Cooley-Tukey FFT:
  Assumes N (number of samples) is a power of 2.
  Recursively breaks DFT into smaller DFTs.
Twiddle Factors:
  Precomputed values of e−j2πkn/N.
Output Interpretation:
  Magnitude ∣X[k]∣: Amplitude of frequency components.
  Phase ∠X[k]: Phase shift of components.

## Slide 6: Short-Time Fourier Transform (STFT)
What is STFT?
  Analyzes signals with time-varying frequency content.
  Segments signals into smaller time windows.
Applications:
  Audio processing (speech, music, noise reduction).
  Biomedical signal analysis (EEG, ECG).
  Mechanical vibration analysis (fault detection).
  Seismic and geophysical applications.

## Slide 7: Applications of STFT
Audio Signal Analysis:
  Speech analysis and synthesis.
  Music signal processing (harmonics, rhythm).
  Noise reduction.
Biomedical Signal Analysis:
  EEG signal processing (epileptic seizures).
  Heart Rate Variability (HRV) analysis.
Mechanical Vibration Analysis:
  Condition monitoring.
  Rotational machinery diagnostics.

## Slide 8: Frequency Domain Analysis with Arduino
ArduinoFFT Library:
  Optimized FFT implementation for Arduino.
Signal Acquisition:
  Analog-to-Digital Conversion (ADC) sampling.
  Nyquist criterion: Sampling rate ≥ 2 × highest frequency.
Applications:
  Vibration analysis (machine condition monitoring).
  Bio-signal processing (heart rate, EEG).
  Spectrum monitoring (radio, sound frequencies).

## Slide 9: Audio Signal Analysis with Arduino
Environmental Sound Analysis:
  Microphone module captures audio signals.
  Sampling rate: 8 kHz (for frequencies up to 4 kHz).
  FFT transforms time-domain data to frequency domain.
Applications:
  Noise monitoring (industrial, urban environments).
  Sound classification (wildlife, machinery).

## Slide 10: Vibration Analysis with Arduino
Machine Condition Monitoring:
  Tri-axial accelerometer measures vibrations.
  FFT converts time-domain vibrations to frequency domain.
Fault Detection:
  Imbalance, misalignment, bearing wear.
Predictive Maintenance:
  Continuous monitoring and trend analysis.
  Early detection of mechanical issues.

## Slide 11: Heart Rate Variability (HRV) Analysis
What is HRV?
  Variation in time between successive heartbeats (RR intervals).
  Reflects autonomic nervous system function.
Frequency Domain Analysis:
  Low-Frequency (LF) band: Sympathetic and parasympathetic activity.
  High-Frequency (HF) band: Parasympathetic activity (relaxation).
  LF/HF ratio: Indicator of stress and autonomic balance.
Arduino Implementation:
  MAX30100 pulse oximeter sensor.
  ArduinoFFT library for PSD (Power Spectral Density) analysis.

## Slide 12: Practical Applications of HRV Analysis
Stress Monitoring:
  Real-time tracking of LF and HF bands.
  Stress-relief techniques (deep breathing, meditation).
Long-Term Health Metrics:
  Daily LF/HF ratio trends.
  Chronic stress detection and lifestyle adjustments.

## Slide 13: Comparison with Frequency Domain Analysis
Time Domain Focus: Temporal changes, transient events.
Frequency Domain Focus: Spectral content of signals.
Complementary Techniques: Foundation for Fourier analysis and predictive modeling.

## Slide 14: Summary
Key Takeaways:
  Frequency domain analysis reveals signal characteristics not visible in the time domain.
  FFT and STFT are powerful tools for analyzing stationary and non-stationary signals.
  Arduino enables practical, real-time frequency domain analysis in various applications.
Applications:
  Audio processing, biomedical signal analysis, machine vibration monitoring, and more.